## Slide 1: The ghost is the machine: Weird machines in transient execution
Ping-Lun Wang, Fraser Brown, Riad S. Wahby
WOOT, 05/25 2023

## Slide 2: What are weird machines?
Definition: models a system’s unintentional behavior, usually triggered from adversarial input
Use weird machines as computation primitives
Perform program obfuscation or secret computations
  The MOV instruction[1]
  Page fault handler [2]
  Time (TSX WM)[3]
[1] S. Dolan, “mov is Turing-complete” (2013)
[2] J. Bangert et al., “The page-fault weird machine: Lessons in instruction-less computation” (WOOT 2013)
[3] D. Evtyushkin et al., “Computing with time: Microarchitectural weird machines” (ASPLOS 2021)

## Slide 3: TSX weird machines that compute with time[3]
[3] D. Evtyushkin et al., “Computing with time: Microarchitectural weird machines” (ASPLOS 2021)
TSX Weird Gate
Input I1 in cache?
Input I2 in cache?
Fetch output Out into cache?
Cache
I1
I2
Cache hit
→ short latency
→ 1
Cache miss
→ long latency
→ 0
= 1
= 0

## Slide 4: TSX weird machines that compute with time[3]
Cache
I1
I2
Out
I1
I2
Out
Cache
I1
I2
Out
I1
I2
Out
[3] D. Evtyushkin et al., “Computing with time: Microarchitectural weird machines” (ASPLOS 2021)
TSX Weird Gate
Input I1 in cache?
Input I2 in cache?
Fetch output Out into cache?
AND
OR

## Slide 5: TSX weird machines that compute with time[3]
Compute on cache states (μArch)
Not visible in architectural states!
Gates: Assign, AND, OR, XOR
[3] D. Evtyushkin et al., “Computing with time: Microarchitectural weird machines” (ASPLOS 2021)
TSX Weird Gate
Input I1 in cache?
Input I2 in cache?
Fetch output Out into cache?

## Slide 6: TSX weird machines that compute with time[3]
Limitations
TSX instructions are easy to detect
  Vulnerable to static analysis!
Limited to some Intel CPUs
  AMD and ARM CPUs are not supported!
[3] D. Evtyushkin et al., “Computing with time: Microarchitectural weird machines” (ASPLOS 2021)
TSX Weird Gate
Input I1 in cache?
Input I2 in cache?
Fetch output Out into cache?

## Slide 7: Our work: generalize TSX WM to Transient WM
Transient weird machine (WM)
TSX → any transient execution primitive!
  Prevent static analysis
  Support AMD, ARM, and Intel CPUs
  95~99% accuracy on all CPUs
New NOT gate design
  Idea: cache state controls the length of transient execution
  Leads to a ≈7X faster XOR gate
Transient execution primitives
TSX
Meltdown
Spectre
Side channel
Cache
Weird gates
Assign
AND
OR
XOR
NOT
①
②
③
④

## Slide 8: What is transient execution?
clflush(X);
TSX { AX /= 0; X[0] = 0;
}
Cache
PC →
(Waiting…)
(Speculative)
X
DIV by 0!!
▲ Transient execution (TSX)
(Modified!!)
Transient execution begins!
Transient execution ends!

## Slide 9: Generalize TSX WM to other primitives
clflush(X);
TSX { AX /= 0; X[0] = 0;
}
▲ Transient execution (TSX)
INIT: SIGFPE { goto EXIT; } clflush(X); AX /= 0; X[0] = 0;
EXIT:
…
▲ Transient execution (Meltdown)

## Slide 10: Assign: input latency controls output variable
INIT: I[0] = 0; SIGFPE { goto EXIT; } clflush(Y); AX /= 0; Out[I[0]] = 0; EXIT: ...
① I is in cache
② I is NOT in cache
Cache
I
Out
Cache
I
Out
DIV by 0!!
Fetch I[0]
Fetch Out[0]
Assign gate
Transient exec.
Assign
DIV by 0!!
Transient exec.
Assign
Fetch I[0]
Fetch Out[0]
❌
✔️
= 0
= 0

## Slide 11: From Assign to OR & AND gates
Out[I1[0]] = 0;
Out[I2[0]] = 0;
Out[I2[I1[0]]] = 0;
OR gate
AND gate
INIT: I[0] = 0; SIGFPE { goto EXIT; } clflush(Y); AX /= 0; Out[I[0]] = 0; EXIT: ...
Assign gate

## Slide 12: How to construct a NOT gate?
DIV by 0!!
Transient exec.
I in cache → fast
Assign
✔️
Assign
I not in cache → slow
❌
AX /= 0; Out[I[0]] = 0;
▲ Assign gate
Time
How to fetch output when input is slow?
→ Fetch output when input is not in cache
Too slow to fetch output…

## Slide 13: How to construct a NOT gate?
I not in cache → slow
DIV by 0!!
NOT
Fetch output
I in cache → fast
DIV by 0!!
❌
✔️
Transient exec.
Transient exec.
AX /= I[0]; Out[tmp[0]] = 0;
▲ NOT gate
Time
Input
↓
Insight: transient execution time is not constant!
Slow input →
Slow transient exec.

## Slide 14: NOT: input latency controls transient execution time
INIT: I[0] = O[0] = 0; SIGFPE { goto EXIT; } clflush(O); clflush(tmp); AX /= I[0]; Out[tmp[0]] = 0; EXIT: ...
① I is in cache
② I is NOT in cache
NOT gate
Cache
I
tmp
Out
Cache
I
tmp
Out
Transient exec.
NOT
Transient exec.
NOT
Fetch I[0]
Fetch tmp[0]
Fetch Out[0]
DIV by 0!!
Division
Fetch Out[0]
Fetch tmp[0]
Fetch I[0]
Division
DIV by 0!!
✔️
❌
Notes: Specially designed NOT gate that relies on different length of transient execution. With the NOT gate, we can construct any circuits.

## Slide 15: Measuring accuracy and runtime
Test on 3 CPUs
  AMD EPYC 7R13
  ARM Graviton 1
  Intel Xeon E7-8800
Implementation
  C/C++ and asm
  1,379 LoC
  Available on GitHub*
Weird Gates
1M operations
Repeat 1,000 times
Median accuracy & runtime
*https://github.com/joeywang4/Transient-Weird-Machine
Notes: Experiment results

## Slide 16: Accuracy and runtime
Accuracy
Gate | AMD | Intel | ARM
AND | 99.96% | 99.99% | 98.89%
OR | 100.00% | 99.99% | 99.46%
Assign | 99.99% | 99.99% | 99.42%
NOT | 99.51% | 99.99% | 99.29%
XOR | 94.36% | 95.58% | 97.97%
MUX | 98.17% | 99.93% | 97.64%
Gate | AMD | Intel | ARM
AND | 1.801 | 2.628 | 32.521
OR | 1.756 | 2.551 | 32.506
Assign | 1.751 | 2.637 | 32.378
NOT | 1.779 | 2.741 | 32.573
XOR | 7.403 | 15.648 | 130.898
MUX | 5.870 | 11.975 | 131.150
Runtime (s/Mops)

## Slide 17: Application: program obfuscation
Obfuscate computations and control flows
Future work: compiler to construct circuits of weird gates
if (input ^ password) {
fail();
} else {
success();
}
XOR
MUX
input
password
success
fail
Function pointer
Obfuscate with Transient WM
Notes: Program obfuscation
Use memory operations to compute

## Slide 18: Takeaways
TSX WMs + Meltdown & Spectre → Transient WMs
Novel NOT gate design
Obfuscate malware and attack exploits
Thank you for listening!
Github: https://github.com/joeywang4/Transient-Weird-Machine
Authors: Ping-Lun Wang, Fraser Brown, Riad S. Wahby
Contact: pinglunw@andrew.cmu.edu

## Slide 19: What is transient execution?
INIT: SIGFPE { goto EXIT; } clflush(X); AX /= 0; X[0] = 0;
EXIT:
…
Cache
PC →
(Waiting…)
(Speculative)
X
DIV by 0!!
▲ Transient execution (Meltdown)
(Modified!!)
Transient execution begins!
Transient execution ends!

## Slide 20: Can Meltdown & Spectre perform computations?
raise_exception(); // the line below is never reached access(probe_array[data * 4096]);
if (x < array1_size) y = array2[array1[x] * 4096];
Spectre
Meltdown
Can we hide computations here?
Not visible in architectural states!
Encryption or decryption
Malicious code
Notes: Background: transient execution attacks and TSX microarchitectural WMs

## Slide 21: Microarchitectural weird machines
Computing with time: Microarchitectural weird machines (ASPLOS’21)
✔️ Can compute AND, OR, XOR and other operations
✔️ Compute with microarchitectural states
  ❌ TSX instructions are easy to detect
  ❌ Only support some Intel CPUs
Q: Can we achieve the same computations without TSX?
A: Yes! Any transient execution primitives are possible!
Q: Can we add support to other CPUs?
A: Yes! AMD, ARM, and Intel CPUs are all supported!

## Slide 22: TSX gates: the Assign gate
INIT: X[0] = 0; clflush(Y); TSX { tmp /= 0; Y[X[0]] = 0; }
…
DIV by 0!
PC
Exit TSX
Pipeline
X is NOT in cache
X is in cache
Y[X[0]] = 0;
Y[0] = 0;
X[0] = 0
Y[X[0]] = 0;
X[0] = ???
Fetch Y[0] in cache!
Y[0] is not fetched…
▲ Assign gate
Notes: The design of our WM. How do gates work